## Slide 1: Network Security
CSE 465 – Information Assurance
Fall 2017
Adam Doupé
Arizona State University
http://adamdoupe.com

## Slide 2: The Internet Protocol Suite
Set of protocols used to transport data between nodes of a network
Also known as the TCP/IP Protocol Suite
Based on abstraction and encapsulation
Link protocols
Internet protocols
Transport protocols
Application protocols

## Slide 3: TCP/IP Layering
TCP
UDP
IP
HTTP
NFS
Hardware Interface
SMTP
DNS
IGMP
ICMP
Physical Layer
ARP
RARP
Link
Internet
Transport
Application

## Slide 4: IP Addresses
Each host has one or more IP addresses for each network interface
IPv4 addresses are composed of 32 bits (class+netid+hostid)
Represented in dotted-decimal notation: 149.169.175.207
Classes
  Class A (0): netid=7 bit (128 networks, actually 1-126), hostid=24 bit (16777216 hosts)
  Class B (10): netid=14 bit (16384 networks), hostid=16 bit (65536 hosts)
  Class C (110): netid=21 bit (2097152 networks), hostid=8 bit (256 hosts)
  Class D - Multicast (1110): multicast addresses
  Class E (1111): reserved or future use

## Slide 5: Classless Inter-Domain Routing (CIDR)
Allocation of large chunks of IP addresses wasted an enormous number of IP addresses
Number of hosts is increasing
IPv6 provides a larger address space but adoption is slow
CIDR is an addressing scheme from 1993 for the Internet which allows for more efficient allocation of IP addresses than the old “Class A, B, and C” address scheme
The netid/hostid boundary can be placed on any bit between 13 and 27
  32 hosts minimum
  524,288 hosts maximum

## Slide 6: Internet Protocol (IP)
The IP protocol represents the “glue” of the Internet
The IP protocol provides a connectionless, unreliable, best-effort datagram delivery service (delivery, integrity, ordering, non-duplication, and bandwidth is not guaranteed)
IP datagrams can be exchanged between any two nodes (provided they both have an IP address)
For direct communication IP relies on a number of different lower-level protocols, e.g., Ethernet, Token Ring, FDDI, RS-232, 802.11

## Slide 7: IP Datagram – RFC 791
Version
HL
Service type (TOS)
Header checksum
Identifier
Flags
Fragment offset
Time To Live
Protocol
Source IP address
Destination IP address
Options
Padding
Data
Total length
0
4
8
12
16
20
24
28
31

## Slide 8: IP Datagram – RFC 791
Version
HL
Service type (TOS)
Header checksum
Identifier
Flags
Fragment offset
Time To Live
Protocol
Source IP address
Destination IP address
Options
Padding
Data
Total length
0
4
8
12
16
20
24
28
31

## Slide 9: IP Encapsulation
Frame header
Frame data
IP header
IP data

## Slide 10: IP: Direct Delivery
If two hosts are in the same physical network the IP datagram is encapsulated in a lower level protocol and delivered directly
111.10.20.14
111.10.20.121
From 111.10.20.121
To 111.10.20.14
Subnetwork 111.10.20
From 09:45:FA:07:22:23
To 0A:12:33:B2:C4:11
09:45:FA:07:22:23
0A:12:33:B2:C4:11

## Slide 11: Ethernet Frame
dest (6)
src (6)
type (2)
data (46-1500)
CRC (4)
0x0800
IP datagram
0x0806
ARP (28)
0x0808
RARP (28)
PAD (18)
PAD (18)

## Slide 12: Ethernet
Widely-used link-layer protocol
Uses CSMA/CD (Carrier Sense, Multiple Access with Collision Detection)
Destination address: 48 bits (e.g., 09:45:FA:07:22:23)
Source address: 48 bits
Type: 2 bytes (IP, ARP, RARP)
Data:
  Min 46 bytes (padding may be needed)
  Max 1500 bytes
CRC: Cyclic Redundancy Check, 4 bytes

## Slide 13: Address Resolution Protocol
The address resolution protocol (ARP) allows a host to map IP addresses to the link-level addresses associated with the peer’s hardware interface (e.g., Ethernet) to be used in direct delivery
ARP messages are encapsulated in the underlying link level protocol

## Slide 14: ARP Request
hosta# arp -a
hosta# ping 192.168.1.10
8:0:46:7:4:a3 ff:ff:ff:ff:ff:ff arp 60: arp who-has 192.168.1.10 tell 192.168.1.100
0:1:3:1d:98:b8 8:0:46:7:4:a3 arp 60: arp reply 192.168.1.10 is-at 0:1:3:1d:98:b8
8:0:46:7:4:a3 0:1:3:1d:98:b8 ip 98: 192.168.1.100 > 192.168.1.10: icmp: echo request
0:1:3:1d:98:b8 8:0:46:7:4:a3 ip 98: 192.168.1.10 > 192.168.1.100: icmp: echo reply
hosta# arp -a
hostb (192.168.1.10) at 00:01:03:1D:98:B8 [ether] on eth0 hostb# arp -a
hosta (192.168.1.100) at 08:00:46:07:04:A3 [ether] on eth0
ARP request
ARP reply
Host B 192.168.1.10 0:1:3:1d:98:b8
Host C
Host A 192.168.1.100 08:00:46:07:04:A3

## Slide 15: Local Area Network Attacks
Goals
  Impersonation of a host
  Denial of service
  Access to information
  Tampering with delivery mechanisms
Sniffing
Spoofing
Hijacking

## Slide 16: Hubs vs. Switches
Early network switches were simple hubs
  All traffic is broadcasted to all ports
Modern network switches keep track of which interface is connected to each port
  All broadcast traffic is sent to all connected hosts
  All directed traffic is sent to the ports associated with the referenced hardware address

## Slide 17: Network Sniffing
Technique at the basis of many attacks
The attacker sets his/her network interface in promiscuous mode
If switched Ethernet is used, then the switch must be “convinced” that a copy of the traffic needs to be sent to the port of the sniffing host

## Slide 18: Why Sniffing?
Many protocols (FTP, POP, HTTP, IMAP) transfer authentication information in the clear
By sniffing the traffic it is possible to collect usernames/passwords, files, mail, etc.
Usually traffic is copied to a file for later analysis

## Slide 19: Sniffing Tools
Tools to collect, analyze, and reply traffic
Routinely used for traffic analysis and troubleshooting
Command-line tools
  tcpdump: collects traffic
  tcpflow: reassemblesTCP flows
  tcpreplay: re-sends recorded traffic
Graphical tools
  Wireshark
    Supports TCP reassembling
    Provides parsers for a number of protocols

## Slide 20: ARP Spoofing
Goal: sniff all traffic between two hosts in a switched environment
The attack leverages the stateless nature of the ARP protocol
  Replies without a request will be accepted
The attacker host sends spoofed ARP messages to the two victim hosts, poisoning their cache
The victim host sends their IP packets to the attacker host
The attacker host acts has a router

## Slide 21: ARP Spoofing
Host B 192.168.1.10 at 00:01:03:1d:98:b8
Host A 192.168.1.100 at 08:00:46:07:04:A3
Host C 192.168.1.137 at BA:DB:AD:BA:DB:AD
192.168.1.10
00:01:03:1D:98:B8
192.168.1.100
08:00:46:07:04:A3
192.168.1.100
08:00:46:07:04:A3
192.168.1.10
00:01:03:1D:98:B8

## Slide 22: ARP Spoofing
Host B 192.168.1.10 at 00:01:03:1d:98:b8
Host A 192.168.1.100 at 08:00:46:07:04:A3
Host C 192.168.1.137 at BA:DB:AD:BA:DB:AD
192.168.1.10
00:01:03:1D:98:B8
192.168.1.100
08:00:46:07:04:A3
192.168.1.100
08:00:46:07:04:A3
192.168.1.10
00:01:03:1D:98:B8
ARP Reply:
192.168.1.10 is at BA:DB:AD:BA:DB:AD

## Slide 23: ARP Spoofing
Host B 192.168.1.10 at 00:01:03:1d:98:b8
Host A 192.168.1.100 at 08:00:46:07:04:A3
Host C 192.168.1.137 at BA:DB:AD:BA:DB:AD
192.168.1.10
BA:DB:AD:BA:DB:AD
192.168.1.100
08:00:46:07:04:A3
192.168.1.100
08:00:46:07:04:A3
192.168.1.10
00:01:03:1D:98:B8
ARP Reply:
192.168.1.10 is at BA:DB:AD:BA:DB:AD

## Slide 24: ARP Spoofing
Host B 192.168.1.10 at 00:01:03:1d:98:b8
Host A 192.168.1.100 at 08:00:46:07:04:A3
Host C 192.168.1.137 at BA:DB:AD:BA:DB:AD
192.168.1.10
BA:DB:AD:BA:DB:AD
192.168.1.100
08:00:46:07:04:A3
192.168.1.100
08:00:46:07:04:A3
192.168.1.10
00:01:03:1D:98:B8
ARP Reply:
192.168.1.100 is at BA:DB:AD:BA:DB:AD

## Slide 25: ARP Spoofing
Host B 192.168.1.10 at 00:01:03:1d:98:b8
Host A 192.168.1.100 at 08:00:46:07:04:A3
Host C 192.168.1.137 at BA:DB:AD:BA:DB:AD
192.168.1.10
BA:DB:AD:BA:DB:AD
192.168.1.100
BA:DB:AD:BA:DB:AD
192.168.1.100
08:00:46:07:04:A3
192.168.1.10
00:01:03:1D:98:B8
ARP Reply:
192.168.1.100 is at BA:DB:AD:BA:DB:AD

## Slide 26: ARP Spoofing
Host B 192.168.1.10 at 00:01:03:1d:98:b8
Host A 192.168.1.100 at 08:00:46:07:04:A3
Host C 192.168.1.137 at BA:DB:AD:BA:DB:AD
192.168.1.10
BA:DB:AD:BA:DB:AD
192.168.1.100
BA:DB:AD:BA:DB:AD
192.168.1.100
08:00:46:07:04:A3
192.168.1.10
00:01:03:1D:98:B8
Ethernet: BA:DB:AD:BA:DB:AD
IP: 192.168.1.100 Data: SECRET

## Slide 27: ARP Spoofing
Host B 192.168.1.10 at 00:01:03:1d:98:b8
Host A 192.168.1.100 at 08:00:46:07:04:A3
Host C 192.168.1.137 at BA:DB:AD:BA:DB:AD
192.168.1.10
BA:DB:AD:BA:DB:AD
192.168.1.100
BA:DB:AD:BA:DB:AD
192.168.1.100
08:00:46:07:04:A3
192.168.1.10
00:01:03:1D:98:B8
Ethernet: 00:01:03:1D:98:B8
IP: 192.168.1.10
Data: SECRET

## Slide 28: ARP Spoofing
Legitimate ARP replies might restore the ARP cache to the correct value
Most ARP-spoofing tool repeatedly send spoofed ARP replies to keep the ARP cache in the desired state

## Slide 29: IP Spoofing
In an IP spoofing attack a host impersonates another host by sending a datagram with the address of the impersonated host as the source address
111.10.20.14
111.10.20.76
111.10.20.121
From 111.10.20.76
To 111.10.20.14
Subnetwork 111.10.20
From 09:45:FA:07:22:23
To 0A:12:33:B2:C4:11
09:45:FA:07:22:23
0A:12:33:B2:C4:11

## Slide 30: Routing: Indirect Delivery
If two hosts are in different physical networks the IP datagram is encapsulated in a lower level protocol and delivered to the directly connected gateway
The gateway decides which is the next step in the delivery process
This step is repeated until a gateway that is in the same physical subnetwork of the destination host is reached
Then direct delivery is used

## Slide 31: Routing
128.111.41.10 11:21:31:41:51:61
111.10.20.121 AA:BB:CC:DD:EE:FF
From 111.10.20.121
To 128.111.41.10
Source/Destination IP addresses are the same for every copy of the datagram
TTL field is decreased at every step
Link level addresses change at every step
The delivery process is based on the destination address only
A0:B0:C0:D0:E0:F0
A1:B1:C1:D1:E1:F1
From AA:BB:CC:DD:EE:FF To A0:B0:C0:D0:E0:F0
From A1:B1:C1:D1:E1:F1 To 11:21:31:41:51:61

## Slide 32: Types of Routing
Hop-by-hop routing
  The delivery route is determined by the gateways that participate in the delivery process
Source routing
  The originator of a datagram determines the route to follow independently before sending the datagram (IP source routing option)

## Slide 33: Hop-by-hop Routing: The Routing Table
The information about delivery is maintained in the routing table
$ route –n
Kernel IP routing table
Destination Gateway Genmask Flags Iface
192.168.1.24 0.0.0.0 255.255.255.255 UH eth0
192.168.1.0 0.0.0.0 255.255.255.0 U eth0
127.0.0.0 0.0.0.0 255.0.0.0 U lo
0.0.0.0 192.168.1.1 0.0.0.0 UG eth0
Flags
  U: the route is up
  G: the destination is a gateway
  H: the route is to a host (if not set, the route is to a network)
  D: the route was created by a redirect message
  M: the route was modified by a redirect message

## Slide 34: Routing Mechanism
Search for a matching host address
Search for a matching network address
Search for a default entry
If a match is not found a message of “host unreachable” or “network unreachable” is returned (by the kernel or by a remote gateway by using ICMP)
Routing tables can be set
  Statically (at startup, or by using the "route" or "ip route" command)
  Dynamically (using routing protocols)

## Slide 35: TCP/IP Layering
TCP
UDP
IP
HTTP
NFS
Hardware Interface
SMTP
DNS
IGMP
ICMP
Physical Layer
ARP
RARP
Link
Internet
Transport
Application

## Slide 36: User Datagram Protocol (UDP)
The UDP protocol relies on IP to provide a connectionless, unreliable, best-effort datagram delivery service (delivery, integrity, non-duplication, ordering, and bandwidth is not guaranteed)
Introduces the port abstraction that allows one to address different message destinations for the same IP address
Often used for multimedia (more efficient than TCP) and for services based on request/reply schema (DNS, NFS, RPC)

## Slide 37: UDP Message
UDP source port
Checksum
UDP message length
Data
UDP destination port
0
4
8
12
16
20
24
28
31

## Slide 38: UDP Message
UDP source port
Checksum
UDP message length
Data
UDP destination port
0
4
8
12
16
20
24
28
31

## Slide 39: UDP Encapsulation
Frame header
Frame data
IP header
IP data
UDP header
UDP data

## Slide 40: UDP Spoofing
Basically IP spoofing
Spoofed UDP request
Server
Attacker
Trusted client
UDP reply

## Slide 41: UDP Hijacking
Variation of the UDP spoofing attack
UDP request
UDP reply
Spoofed UDP reply
UDP request
Server
Attacker
Client

## Slide 42: UDP Portscan
Used to determine which UDP services are available
A zero-length UDP packet is sent to each port
If an ICMP error message "port unreachable" is received the service is assumed to be unavailable
Many TCP/IP stack implementations implement a limit on the error message rate, therefore this type of scan can be slow (e.g., Linux limit is 80 messages every 4 seconds)

## Slide 43: UDP Portscan
% nmap -sU 192.168.1.10
Starting nmap by fyodor@insecure.org ( www.insecure.org/nmap/ )
Interesting ports on (192.168.1.10):
(The 1445 ports scanned but not shown below are in state: closed)
Port State Service
137/udp open netbios-ns
138/udp open netbios-dgm
Nmap run completed -- 1 IP address (1 host up) scanned in 4 seconds

## Slide 44: Transmission Control Protocol (TCP)
The TCP protocol relies on IP to provide a connection-oriented, reliable stream delivery service (no loss, no duplication, no transmission errors, correct ordering)
TCP, as UDP, provides the port abstraction
TCP allows two nodes to establish a virtual circuit, identified by source IP address, destination IP address, source TCP port, destination TCP port
The virtual circuit is composed of two streams (full-duplex connection)
The couple IP address/port number is sometimes called a socket (and the two streams are called a socket pair)

## Slide 45: TCP Segment
Acknowledgment number
Sequence number
HLEN
Checksum
Options
Padding
Data
Destination port
0
4
8
12
16
20
24
28
31
Source port
Flags
Window
Urgent pointer
Reserved

## Slide 46: TCP Segment
Acknowledgment number
Sequence number
HLEN
Checksum
Options
Padding
Data
Destination port
0
4
8
12
16
20
24
28
31
Source port
Flags
Window
Urgent pointer
Reserved

## Slide 47: TCP Encapsulation
Frame header
Frame data
IP header
IP data
TCP header
TCP data

## Slide 48: TCP Seq/Ack Numbers
The sequence number specifies the position of the segment data in the communication stream (SYN=13423 means: the payload of this segment contains the data from byte 13423 to byte 13458)
The acknowledgment number specifies the position of the next byte expected from the communication partner (ACK = 16754 means: I have received correctly up to byte 16753 in the stream, I expect the next byte to be 16754)
These numbers are used to manage retransmission of lost segments, duplication, flow control

## Slide 49: TCP Flags
Flags are used to manage the establishment and shutdown of a virtual circuit
  SYN: request for the synchronization of syn/ack numbers (used in connection setup)
  ACK: states the acknowledgment number is valid (all segment in a virtual circuit have this flag set, except for the first one)
  FIN: request to shutdown one stream
  RST: request to immediately reset the virtual circuit
  URG: states that the Urgent Pointer is valid
  PSH: request a “push” operation on the stream (that is, the stream data should be passed to the user application as soon as possible)

## Slide 50: TCP Virtual Circuit: Setup
A server, listening to a specific port, receives a connection request from a client: The segment containing the request is marked with the SYN flag and contains a random initial sequence number Sc
The server answers with a segment marked with both the SYN and ACK flags and containing
  an initial random sequence number Ss
  Sc + 1 as the acknowledgment number
The client sends a segment with the ACK flag set and with sequence number Sc + 1 and acknowledgment number Ss + 1

## Slide 51: What Initial Sequence Number?
The TCP standard (RFC 793) specifies that the sequence number should be incremented every 4 microseconds
BSD UNIX systems initially used a number that is incremented by 64,000 every half second (8 microseconds increments) and by 64,000 each time a connection is established

## Slide 52: TCP: Three-way Handshake
Client
Server
13987
22
seq: 6574
ack: 0
SYN:1
ACK:0
FIN:0
22
13987
seq: 7611
ack: 6575
SYN:1
ACK:1
FIN:0
13987
22
seq: 6575
ack: 7612
SYN:0
ACK:1
FIN:0

## Slide 53: TCP Virtual Circuit: Data Exchange
A partner sends in each packet the acknowledgment of the previous segment and its own sequence number increased of the number of transmitted bytes
A partner accepts a segment of the other partner only if the numbers are inside the transmission window
An empty segment may be used to acknowledge the received data

## Slide 54: TCP Virtual Circuit: Data Exchange
Client
Server
13987
22
seq: 6575
ack:7612
SYN:0
ACK:1
FIN:0
22
13987
seq: 7612
ack: 6600
SYN:0
ACK:1
FIN:0
13987
22
seq: 6600
ack: 7642
SYN:0
ACK:1
FIN:0
25 bytes
30 bytes

## Slide 55: TCP Virtual Circuit: Shutdown
One of the partners, A, can terminate its stream by sending a segment with the FIN flag set
The other partner, B, answers with an ACK segment
From that point on, A will not send any data to B: it will just acknowledge data sent by B
When B shutdowns its stream the virtual circuit is considered closed

## Slide 56: TCP Virtual Circuit: Shutdown
Client
Server
13987
22
seq: 6983
ack:8777
SYN:0
ACK:1
FIN:1
22
13987
seq: 8777
ack: 6984
SYN:0
ACK:1
FIN:0
13987
22
seq: 6984
ack: 8808
SYN:0
ACK:1
FIN:0
30 bytes
22
13987
seq: 8807
ack: 6984
SYN:0
ACK:1
FIN:1

## Slide 57: TCP Portscan
Used to determine the TCP services available on a victim host
Most services are statically associated with port numbers (see /etc/services in UNIX systems)
In its simplest form (connect() scanning), the attacker tries to open a TCP connection to all 65535 ports of the victim host
If the handshake is successful then the service is available
Advantage: no need to be root
Disadvantage: very noisy

## Slide 58: connect() Scan
# nmap -sT 192.168.1.20 Starting nmap by fyodor@insecure.org ( www.insecure.org/nmap/ ) Interesting ports on (192.168.1.20): (The 1500 ports scanned but not shown below are in state: closed) Port State Service 7/tcp open echo 9/tcp open discard 11/tcp open systat 13/tcp open daytime 15/tcp open netstat 19/tcp open chargen 21/tcp open ftp 22/tcp open ssh 23/tcp open telnet 512/tcp open exec 513/tcp open login 514/tcp open shell 6000/tcp open X11 Nmap run completed -- 1 IP address (1 host up) scanned in 0 seconds

## Slide 59: TCP SYN Scanning
AKA "half-open" scanning
The attacker sends a SYN packet
If the server answers with a SYN/ACK packet then the port is open or (usually) with a RST packet if the port is closed
The attacker sends a RST packet instead of the final ACK
The connection is never open and the event is not logged by the operating system/application

## Slide 60: TCP SYN Scanning
# nmap -sS 128.111.38.78
Port State Service
80/tcp open http
Nmap run completed -- 1 IP address (1 host up) scanned in 1 second
11:27:32.249220 128.111.48.69.47146 > 128.111.41.38.78: S 3886663922:3886663922(0) win 2048
11:27:32.266910 128.111.48.69.47146 > 128.111.41.38.78: S 3886663922:3886663922(0) win 2048
11:27:32.266914 128.111.48.69.47146 > 128.111.41.38.81: S 3886663922:3886663922(0) win 2048
11:27:32.266918 128.111.48.69.47146 > 128.111.41.38.82: S 3886663922:3886663922(0) win 2048
11:27:32.266923 128.111.48.69.47146 > 128.111.41.38.80: S 3886663922:3886663922(0) win 2048
11:27:32.266925 128.111.48.69.47146 > 128.111.41.38.79: S 3886663922:3886663922(0) win 2048
11:27:32.267904 128.111.41.38.78 > 128.111.48.69.47146: R 0:0(0) ack 3886663923 win 0 (DF)
11:27:32.267970 128.111.41.38.81 > 128.111.48.69.47146: R 0:0(0) ack 3886663923 win 0 (DF)
11:27:32.268038 128.111.41.38.82 > 128.111.48.69.47146: R 0:0(0) ack 3886663923 win 0 (DF)
11:27:32.268106 128.111.41.38.80 > 128.111.48.69.47146: S 1441896698:1441896698(0) ack 3886663923 win 5840 <mss 1460> (DF)
11:27:32.268121 128.111.48.69.47146 > 128.111.41.38.80: R 3886663923:3886663923(0) win 0 (DF)
11:27:32.268174 128.111.41.38.79 > 128.111.48.69.47146: R 0:0(0) ack 3886663923 win 0 (DF)

## Slide 61: OS Fingerprinting
OS fingerprinting allows one to determine the operating system of a host by examining the reaction to carefully crafted packets
  Wrong answers to FIN TCP packets
  "Undefined" flags in the TCP header of a request are copied verbatim in the reply
  Weird combinations of flags in the TCP header
  Selection of TCP initial sequence numbers
  Selection of initial TCP window size
  Analysis of the use of ICMP messages
    Error rate
    Amount of offending datagram included
  TCP options
OS fingerprinting also can be performed in a passive way using tools such as p0f

## Slide 62: TCP Spoofing
Attack aimed at impersonating another host when establishing a TCP connection
First discussed by R.T. Morris in "A Weakness in the 4.2BSD Unix TCP/IP Software" in 1985
Used by Mitnick in his attack against SDSC

## Slide 63: TCP Spoofing
Node A trusts node B (e.g., login with no password if the TCP connection comes from a specific IP)
Node C wants to impersonate B with respect to A in opening a TCP connection
C kills B (flooding, crashing, redirecting) so that B does not send annoying RST segments
C sends A a TCP SYN segment in a spoofed IP packet with B’s address as the source IP and Sc as the sequence number
A replies with a TCP SYN/ACK segment to B with Ss as the sequence number. B ignores the segment: dead or too busy
C does not receive this segment but to finish the handshake it has to send an ACK segment with Ss + 1 as the acknowledgment number
  C eavesdrops the SYN/ACK segment
  C guesses the correct sequence number

## Slide 64: TCP Spoofing
13987
513
seq: 11000
ack: 0
SYN:1
ACK:0
FIN:0
513
13987
seq: 54002
ack: 11001
SYN:1
ACK:1
FIN:0
13987
513
seq: 11001
ack: 54003
SYN:0
ACK:1
FIN:0
138.13.2.67
211.3.56.5
C:117.76.3.3
A: 211.3.56.5
B:138.13.2.67
211.3.56.5
138.13.2.67
138.13.2.67
211.3.56.5
1
2
3
0
Denial-of-Service Attack

## Slide 65: TCP Hijacking
Powerful technique to take control of an existing TCP connection
The attacker uses spoofed TCP segments to
  Insert data in the streams
  Reset an existing connection (denial of service)
The correct sequence/acknowledgment numbers must be used
  The attacker can eavesdrop the traffic between client and server
  The attacker can guess the correct seq/ack numbers
Described in “Simple Active Attack Against TCP” by L. Joncheray

## Slide 66: TCP Hijacking
The attacker waits until the connection is “quiet”
  All the transmitted data have been acknowledged (by both endpoints)
The attacker injects the data in the stream
  “Desynchronizes” the connection
The receiver of the injected data sends an acknowledgment to the apparent sender
The apparent sender replies with an acknowledgement with the “expected” sequence number
The receiver considers this as out-of-sync and sends an an acknowledgement with the “expected” sequence number
....

## Slide 67: TCP Hijacking
ACK messages with no data are not retransmitted in case of loss
The “ACK storm” continues until one message is lost
Any subsequent attempt to communicate will generate an ACK storm
ACK storms can be blocked by the attacker using ACK packets with the right numbers

## Slide 68: TCP Hijacking
(2) ACK=CL_SEQ + 30
(1) Spoofed TCP
with SEQ=CL_SEQ
and 30 bytes of data
(3) Acknowledge SEQ=CL_SEQ!
Server
Attacker
Client
CL_SEQ = SVR_ACK
SVR_SEQ = CL_ACK

## Slide 69: TCP Hijacking
This technique can be used against both client and server to completely hijack the communication channel (man-in-the-middle attack)
"Early desynchronization" can be achieved by the attacker by resetting existing connections and immediately opening new ones (between the same ports) with different initial sequence numbers

## Slide 70: SYN-flooding Attack
Very common denial-of-service attack, aka Neptune
Attacker starts handshake with SYN-marked segment
Victim replies with SYN-ACK segment
Attacker… stays silent
  Note that the source IP of the attacker can be spoofed, since the final ACK is not required
A host can keep a limited number of TCP connections in half-open state.
  After that limit, it cannot accept any more connections

## Slide 71: SYN-flooding Attack
Current solutions
  Filtering
  Increase the length of the half-open connection queue
  Reduce the SYN-received timeout
  Drop half-open connections when the limit has been reached and new requests for connection arrive
  Limit the number of half-open connections from a specific source
  Use SYN cookies
See TCP SYN Flooding Attacks and Common Mitigations, RFC 4987

## Slide 72: SYN Cookies
Special algorithm used for determining the initial sequence number of the server
The number is
  Top 5 bits: t mod 32, where t is a 32-bit time counter that increases every 64 seconds
  Following 3 bits: the encoding of the Maximum Segment Size (MSS) chosen by the server in response to the client's MSS
  A keyed hash of:
    Counter t
    Source/Destination IP addresses and ports

## Slide 73: SYN Cookies
A server that uses SYN cookies sends back a SYN+ACK, exactly as if the SYN queue had been larger
When the server receives an ACK, it checks that the secret function works for a recent value of t, and then rebuilds the SYN queue entry (using the encoded MSS info)
Drawbacks:
  The server sequence number grows faster than normal
  The MSS value is limited by the encoding procedure (only 8 possible values)
  No data can be included in the initial SYN

## Slide 74: State Attacks
There are other attacks that exploit the fact that the server has to maintain a certain amount of memory/resources associated with each open TCP connection
  Memory for the socket descriptor
  Process or thread to manage the connection
  Memory associated with the data in the TCP stream that has not yet been acknowledged
  …

## Slide 75: Firewalls
Mechanism to enforce network access policy

## Slide 76: Network Security Research